## Slide 1
CmdType_Reg_Request
패킷 형태 정리 – TIFD, TIRD에서 서버에 처음 접속 시
(*) = Tifd 또는 Tird
CmdType_Reg_Confirm
PktHead head;
head.command = CmdType_Reg_Request;
head.answer = 0;
head.category = Device::DeviceNone;
head.payloadSize = 0;
Total Size = 8
PktHead head;
head.command = CmdType_Reg_Confirm;
head.answer = 0;
head.category = Device::DeviceNone;
head.payloadSize = 0;
Total Size = 8
CmdType_Reg_Request
PktHead head;
head.command = CmdType_Reg_Request;
head.answer = 0;
head.category = Device::Device(*);
head.payloadSize = sizeof(St(*)Data);
Total Size = 8 + St(*)Data
Server
Client
CmdType_(*)_Info
PktHead head;
head.command = CmdType_Reg_Request;
head.answer = 0;
head.category = Device::Device(*);
head.payloadSize = sizeof(St(*)Data);
Total Size = 8 + St(*)Data

## Slide 2
패킷 형태 정리– 페어링 관련
(*) = Tifd 또는 Tird
CmdType_Pairing
CmdType_LoRa_CH
PktHead head;
head.command = CmdType_Pairing;
head.answer = 0;
head.category = ePairState::PairState_Pair;
head.payloadSize = 16; (deviceId<12> + length<4>)
Total Size = 8 + 16;
PktHead head;
head.command = CmdType_Lora_CH
head.answer = 0;
head.category = 0;
head.payloadSize = 1;
(Lora channel = 2~16)
Total Size = 8 + 1
TIFD에게만
전송
두개 모두
전송
성공
알람
CmdType_Alram
PktHead head;
head.command = CmdType_Alram;
head.answer = 0;
head.category = 0;
head.payloadSize = 0;
Total Size = 8
전부 서버에서 Send

## Slide 3
패킷 형태 정리– 페어링 중, 종료되었을 경우
(*) = Tifd 또는 Tird
CmdType_Lora_CH
PktHead head;
head.command = CmdType_Lora_CH
head.answer = 0;
head.category = 0;
head.payloadSize = 1;
(LORA_DEFAULT_CH = 1)
Total Size = 8 + 1
Tifd 종료
Tird 종료
TIRD에게
전송
CmdType_Pairing
Command_LoRa_CH
PktHead head;
head.command = CmdType_Pairing;
head.answer = 0;
head.category = ePairState::PairState_UnPair;
head.payloadSize = 0;
Total Size = 8;
PktHead head;
head.command = CmdType_Lora_CH
head.answer = 0;
head.category = 0;
head.payloadSize = 1;
(LORA_DEFAULT_CH = 1)
Total Size = 8 + 1
전부 서버에서 Send
TIFD에게
전송

## Slide 4
struct StTirdData
{
uint8_t nTirdVer[4];
char deviceId[12];
float lat;
float lon;
float alt;
float speed;
int32 sat;
int32 nLoraCh;
int8 nLoraPower;
uint8 nLoraSF;
uint8 nLoraBW;
uint8 nLoraCR;
float battery;
StTime stTime;
};
struct StTifdData
{
uint8_t nTifdVer[4];
char deviceId[12];
int32 trainNo;
int32 trainLength;
int32 trainStatus;
float lat;
float lon;
float alt;
float speed;
int32 sat;
int32 distance;
uint8 nLoraVer[4];
int32 nLoraCh;
int8 nLoraPower;
uint8 nLoraSF;
uint8 nLoraBW;
uint8 nLoraCR;
char nTirdRcvId[12];
int8 nRssi;
StTime stTime;
};

## Slide 5
enum CommandType : uint16
{
  CmdType_Tifd_Info = 0x01,
  CmdType_Tird_Info = 0x02,
  CmdType_LoRa_CH = 0x03,
  CmdType_Paring = 0x04,
  CmdType_Alarm = 0x05,
  CmdType_Reg_Request = 0x06, CmdType_Reg_Confirm = 0x07,
  CmdType_KeepAlive = 0xff
};